## Slide 1: ODFW Instream habitat data as part of monitoring under the Oregon Plan for Salmon and Watersheds

## Slide 2: Spatial and Temporal Design
3-year
9-year
Once
Annual
Lower Columbia
  89 sites per year
  774 unique sites
Oregon Coast
  166 sites per year
  1,726 unique sites
South Coast
  55 sites per year
  643 unique sites
Spatially balanced (GRTS)
Rotating panel: sites sampled at different intervals
Wadeable 1st – 3th Order streams
1998 – 2018 (present)

## Slide 3
Survey Details
500 m (outside anadromy distribution) or 1,000 m (inside anadromy distribution) reach lengths
Physical habitat
Since 2014, parr quantified in pools at all habitat sites

## Slide 4: All Metrics
General survey details | Reach context | Geomorphic channel | Substrate | Wood | In survey observations
Primary channel length | Valley reach index | Number of units per 100 m | Weighted percent sand, organics in riffles | Pieces of large woody debris | Total number of beaver dams
Secondary channel length | Active channel width | Number of habitat units | Weighted percent gravel in riffles | Volume of large woody debris | Total number of signs of beaver activity
Primary channel area | Active channel height | Number of pools | Count of large boulders per 100 meters | Pieces of large wood per 100 meters | Total number of culverts
Secondary channel area | Terrace width | Percent of pools | Weighted percent sand, organics | Volume of large wood per 100 meters | Total number of visible mass failures
Percent secondary channel area | Terrace width | Percent of scour pools | Weighted percent gravel | Number of key pieces | Total number of visible debris jams
Gradient | Flood-prone width | Percent of slack water pools | Weighted percent cobble | Pieces of key large wood (>60 cm X 12 m) per 100 meters | Total number of artificial habitat structures
Wetted width | Flood-prone height | Scour pool depth | Weighted percent boulder |  | 
Width:Depth ratio |  | Deep pools per kilometer | Weighted percent bedrock |  | 
Percent shading |  | Complex pools, pools with more than 3 pieces of wood |  |  | 
UTM Northing |  | Complex pools per kilometer |  |  | 
UTM Easting |  | Channel width per pool |  |  | 
 |  | Pools per 100 m of reach length |  |  | 
 |  | Residual pool depth |  |  | 
 |  | Riffle depth |  |  | 

## Slide 5
Spatial distribution of sites in Siletz
All Years

## Slide 6
Spatial distribution of sites in Siletz
1998

## Slide 7
Spatial distribution of sites in Siletz
2003

## Slide 8
Spatial distribution of sites in Siletz
2005

## Slide 9
Spatial distribution of sites in Siletz 2010

## Slide 10
Spatial distribution of sites in Siletz
2017

## Slide 11
Anlauf-Dunn et al. 2011
Relationship with different landscape predictors

## Slide 12: All Metrics Suggested Metrics Highlighted
General survey details | Reach context | Geomorphic channel | Substrate | Wood | In survey observations
Primary channel length | Valley reach index | Number of units per 100 m | Weighted percent sand, organics in riffles | Pieces of large woody debris | Total number of beaver dams
Secondary channel length | Active channel width: ACW | Number of habitat units | Weighted percent gravel in riffles: WGTED_SLOPE_GRAVEL | Volume of large woody debris | Total number of signs of beaver activity
Primary channel area | Active channel height | Number of pools | Count of large boulders per 100 meters | Pieces of large wood per 100 meters | Total number of culverts
Secondary channel area | Terrace width | Percent of pools | Weighted percent sand, organics | Volume of large wood per 100 meters: LWDVOL1 | Total number of visible mass failures
Percent secondary channel area: PCTSCCHNLA | Terrace width | Percent of scour pools | Weighted percent gravel | Number of key pieces | Total number of visible debris jams
Gradient | Flood-prone width | Percent of slack water pools PCTSWPOOL | Weighted percent cobble | Pieces of key large wood (>60 cm X 12 m) per 100 meters | Total number of artificial habitat structures
Wetted width | Flood-prone height | Scour pool depth | Weighted percent boulder |  | 
Width:Depth ratio |  | Deep pools per kilometer POOL1P_KM | Weighted percent bedrock WGTED_SLOPE_BEDROCK |  | 
Percent channel shade |  | Complex pools, pools with more than 3 pieces of wood |  |  | 
UTM Northing |  | Complex pools per kilometer |  |  | 
UTM Easting |  | Channel width per pool |  |  | 
 |  | Pools per 100 m of reach length: POOLS100 |  |  | 
 |  | Residual pool depth |  |  | 
 |  | Riffle depth: RIFFLEDEP |  |  |